# Two-Wheeler Digital Instrument Cluster
Technical Summary Document (PoC Document)

## 1. Objective / Use Case
The objective of this Proof of Concept (PoC) is to design and demonstrate a two-wheeler digital instrument cluster that displays real-time vehicle parameters such as speed, temperature,humidity, battery level, and connectivity with WiFi and Bluetooth.
The system focuses on:
- Real-time sensor data acquisition using ESP32
- Data visualization using Qt/QML-based HMI
- Desktop and embedded Android board validation
This PoC is limited to data acquisition, processing, and display. Vehicle control, ECU integration, and production-grade safety mechanisms are out of scope.

## 2. Problem Understanding
Modern two-wheeler increasingly rely on digital clusters to display vehicle status and rider information. Key challenges addressed in this PoC include:
- Acquiring real-time sensor data from external hardware
- Processing analog and motion sensor inputs accurately
- Displaying data smoothly on a Qt/QML-based UI
- Ensuring compatibility across desktop and embedded Android platforms
- Avoiding false or unstable readings due to sensor noise

## 3. Hardware & Platform Used
### 3.1 Sensor & Controller Unit
- ESP32 DevKit V1
- Potentiometer
  - Used to simulate accelerator / throttle input
  - Converted into vehicle speed
- MPU6050 Motion Sensor
  - Accelerometer data used
  - Provides temperature and motion-related information
- Communication:
  - USB Serial / Wi-Fi (PoC evaluation)
Reason for selection:
- ESP32 provides integrated ADC, Wi-Fi, and sufficient processing capability
- MPU6050 is widely used, stable, and suitable for automotive PoCs
- Potentiometer enables controlled speed simulation

### 3.2 Display Platform
- Qt 5.15 (Qt Quick / QML)
- Platforms tested:
  - Linux Desktop (Ubuntu)
  - Embedded Android OS board (AOSP-based)

## 4. High-Level Architecture
1. ESP32 reads sensor values:
  1. Throttle position (potentiometer)
  2. Temperature and motion data (MPU6050)
2. Sensor data is processed and formatted
3. Data is transmitted to the application layer
4. Qt/QML HMI visualizes:
  1. Speedometer
  2. Temperature indicator
  3. Battery level (derived from speed)
  4. Connectivity status

## 5. Core Functional Logic
### 5.1 Speed Calculation
- Potentiometer ADC value (0–4095) mapped to speed range:
  - 0–120 km/h
- Provides smooth and continuous speed variation
- Mimics real two-wheeler accelerator behavior

### 5.2 Temperature Monitoring
- Temperature data obtained from MPU6050 sensor
- Displayed in real-time on the cluster UI
- Used for monitoring engine/environment conditions (PoC simulation)

### 5.3 Battery Level Simulation
- Battery percentage calculated based on speed:
  - Higher speed → faster battery drain
- Demonstrates realistic EV-style battery behavior
- Battery updates dynamically with speed changes

### 5.4 Sensor Stability Handling
Observed challenges:
- Minor fluctuations in sensor values
- ADC noise from potentiometer
Mitigation:
- Value smoothing
- Threshold-based updates
- Periodic sampling instead of continuous redraw

## 6. UI / HMI Design
- Developed using Qt Quick and QML
- Optimized for:
  - Automotive landscape display
  - Clear readability
  - Minimal distraction
- Components:
  - Circular speedometer
  - Digital temperature readout
  - Battery indicator
  - Status icons (Wi-Fi / connectivity)

## 7. Data Communication Approach
### 7.1 Firebase-Based Data Sync (Attempted)
- Firebase used for real-time cloud data synchronization
- Desktop testing successful
Limitation observed:
- On the embedded Android OS board, Firebase real-time listeners did not update sensor values
- Speed and temperature remained at default values (0)
Reason identified:
- AOSP-based embedded Android lacks full Google Play Services support
- Firebase is optimized for mobile Android devices, not embedded platforms

### 7.2 Local Communication (Preferred for PoC)
- USB Serial / local Wi-Fi communication
- Ensures deterministic real-time updates
- Suitable for embedded and automotive use cases

## 8. Validation & Results
### 8.1 Normal Operation
- Potentiometer adjusted gradually
- Speed updates smoothly on UI
- Temperature displayed correctly
- Battery drains proportionally to speed
### 8.2 Dynamic Testing
- Rapid throttle changes
- UI remains responsive
- No crashes or freezes observed
- Data consistency maintained

## 9. Challenges Faced & Resolutions
Challenge	Resolution
Sensor noise	Threshold filtering & mapping
Firebase real-time issues	Platform limitation identified
Embedded Android constraints	Shifted to local communication
Qt + hardware integration	Modular C++ backend with QML binding
Cross-platform differences	Separate desktop & embedded validation

## 10. Final Outcome
- Successfully demonstrated a two-wheeler digital cluster PoC
- Real-time speed, temperature, and battery simulation achieved
- ESP32 sensor integration validated
- Qt/QML HMI proven suitable for automotive displays
- Platform limitations clearly identified and documented

## 11. Future Enhancements
- CAN bus integration
- GPS-based speed validation
- Real battery BMS data
- Bluetooth-based sensor communication
- Production-grade power optimization
- Secure cloud data sync via gateway

## 12. Conclusion
This PoC demonstrates a practical and scalable approach to building a two-wheeler digital instrument cluster using ESP32 hardware and Qt/QML-based HMI.
The project highlights both hardware integration capability and embedded software understanding, while clearly identifying real-world platform constraints.

End of Document
If you want, next I can:
- Shorten this to 1-page manager version
- Convert it to PPT demo explanation
- Add flow diagram explanation in words